PRESS RELEASE
May 2010

## New Source for Carbon Fibres in Europe

Dreychem (www.dreychem.com) has added chopped and milled carbon fibres to its portfolio of products. The European distribution contract between the Japanese Nippon Polymer Sangyo Co., Ltd., and Dreychem was signed in April 2010. Limited quantities of these fibres, which are used to improve the characteristics of engineering and high performance polymers, are now available for production tests. Full commercial delivery is scheduled for midyear.

The average length of the milled carbon fibres is 90 µm with a bulk density of 250 kg/m³. Among the main applications of these fibres, which are delivered in packages of 10 kg, are compounds with high performance polymers such as liquid crystal polymers (LCP), polyphenylene sulfide (PPS) or polyphenylene oxide (PPO), providing increased conductivity as well as improved friction and wear properties.

The chopped carbon fibres are delivered in packages of 20 kg with standard lengths of app. 3 mm to 6 mm. Customer specific, mainly higher lengths are available upon request. Depending on the polymer matrix to be reinforced, sizing agents are epoxy and/or polyurethane. Accordingly, applications of these fibres range from polypropylene (PP), acrylonitrile butadiene styrene copolymers (ABS), nylon (PA), polybutylene terephthalate (PBT), polycarbonate (PC) and polyoxymethylene (POM) through to polyphenylene oxide (PPO).

The mechanical properties of the basic (PAN) filaments range from 3,400 MPa to 4,500 MPa for tensile strength and from 230 GPa to 290 GPa for stiffness. Their specific electrical resistance is close to 1.7 x 10-3 Ohm x cm.

For further Information please contact:

Kerstin Brunken, Dreychem GmbH, Briggstr. 5, D-26802 Moormerland,

Tel.: +49 (0) 49 54 - 89 44 34, Fax: +49 (0) 49 54 - 9 55 98 07, E-Mail: brunken@dreychem.com

Editorial contact and voucher copies:

Dr. Jörg Wolters, Konsens PR GmbH & Co. KG, Hans-Kudlich-Straße 25, D-64823 Groß-Umstadt

Tel: +49 (0) 60 78/93 63-0, Fax: -20, E-Mail: joerg.wolters@konsens.de

Chopped and milled carbon fibres which improve the performance of thermoplastic polymers are a recent addition to Dreychem’s product portfolio.

Image: Dreychem