PRESS RELEASE

HRSflow at FAKUMA 2015 – Hall A2, Stand 2217:

Intelligent hot runner systems for precision injection molding

Buchschwabach/Germany, August 2015 – At this year’s Fakuma, the Italian hot runner specialist HRSflow, represented by its German sales subsidiary HRSflow GmbH, Roßtal-Buchschwabach, will focus on high-performance hot runner systems both for the cascade injection molding of large-format parts and for multi-cavity applications. Members of the team will demonstrate the mode of action of the further developed FLEXflow technology, a servo-driven, finely regulated valve gate system. One popular field of application is that of the injection molding of complex automotive components. The latest development, which is being presented in public for the first time at Fakuma, is the integration of FLEXflow into Moldflow simulation software. The HRSflow line, Multitech – which is now independent – will showcase among other things the use of the very latest technologies to shorten the cooling time in multi-cavity molds.

A major advantage of the FLEXflow valve gate system is that it can be used to produce large-area parts with a high-quality surface. Especially with cascade injection molding, the electrically driven needle valve nozzles allow the individual, precise and sequentially coordinated opening and shutting of the valve gates at selectable speeds. As a result, the melt flow in the individual hot runner nozzles and the volume flow in the mold cavity can be controlled with outstanding accuracy. This optimized filling process not only produces a better part surface than with the conventional cascade injection molding process, it also has the advantage that, with FLEXflow, through the much wider process window, the required clamping force and even the part weight can be reduced without any loss of quality. Through the integration of this technology into Moldflow simulation software, the prediction of the course of the injection molding process in the mold that is so important for the mold design is significantly improved.

In the Multitech line, HRSflow offers hot runner solutions for injection molding designed for the fast cycle time and high production volume of packaging, caps and closures, and articles for medical technology, the electrical and electronics industry and automotive construction. The focus here is on high numbers of cavities, short cycle times, uniform balancing and rapid color changes. At Fakuma, new solutions will also be showcased for cooling the mold to shorten cycle times. This is attained by innovative cooling channel inserts, produced by the SLM technology (selective laser melting), similar to the technique known as 3D printing. Also to be presented at Fakuma for the first time is a hot runner nozzle designed specifically for thick-wall applications.

About HRSflow

HRSflow (www.hrsflow.com) is a division of INglass S.p.A. (www.inglass.it), headquartered in San Polo di Piave/Italy. It is specialized in the development and production of advanced and innovative hot runner systems for the injection molding industry. The group of companies has over 1,000 employees and is present on all the major global markets. HRSflow produces hot runner systems at its European headquarters in San Polo di Piave/Italy, in Asia at its plant in Hangzhou/China and, since mid-2015, at its newly built facility in the United States, at Byron Center near Grand Rapids, Michigan.

______________

Contact and further information

Grit Feistkorn, Automotive Marketing Manager

Phone: +49 160 7407058, E-Mail: grit.feistkorn@hrsflow.com

Caterina Boschetti – Marketing & Communications Dept.

Phone: +39 0422 750120, E-mail: caterina.boschetti@inglass.it

HRSflow GmbH Sales Germany

Stuttgarter Str. 33, D-90574 Roßtal-Buchschwabach/Germany

Phone: +49 9127 902000, E-Mail: germany@hrsflow.com

www.hrsflow.com

Editrial contact and voucher copies:

Dr. Georg Krassowski, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25,  D-64823 Groß-Umstadt/Germany – www.konsens.de

Phone: +49 (0) 60 78 / 93 63 - 0,  Fax: - 20,  E-Mail: georg.krassowski@konsens.de

Dear Colleagues,

Press releases from HRSflow with text (German and English) 
as well as pictures in print-ready resolution are available to download from:

www.konsens.de/hrsflow.html

Cascade injection molding with FLEXflow, the servo-driven hot runner needle valve system, produces large-format parts with a reproducible high-quality surface. (photo: HRSflow)