Recycling agricultural film at a top quality level

Großbottwar, Germany, June 2013
In Champlon/Belgium, Soreplastic S.A. runs one of Europe's most advanced and powerful recycling plants for used agricultural film. Here, a custom optimized Power Universo 2800 single-shaft shredder from Lindner ReSource (www.lindner-resource.com) and a 1716 TVEplus recycling extrusion line from Erema (www.erema.at) substantially contribute to the conversion of collected post-consumer film – often heavily soiled with foreign materials – into a re-granulate of the highest quality.

Recycling this soft, thin and typically highly contaminated agricultural film is a difficult and laborious process since the collected material does not lend itself easily to shredding, separation and cleaning. On the other hand, the plastics involved, such as PE-LD (low-density polyethylene) and PE-LLD (linear low-density polyethylene), are in keen demand, even in their recycled form, if the quality is right. Soreplastic invested a great deal of time in the choice of the proper machinery and equipment, recalls Vincent Sciascia, the company's Managing Director. "High throughput, low sensitivity to impurities, low wear costs and constant high quality of the final product were our main criteria. In addition, we required extensive support from the machine builders –  from advice in the project development phase through customizing the machines for our purposes, but also in terms of local presence from the first start-up to the plant's trouble-free continuous operation. In the final analysis, Lindner ReSource and Erema convinced us in every respect."

Following the separator-based and manual removal of coarse foreign debris, a belt conveyor feeds the material first into the Power Universo 2800, a slow-running single-shaft shredder with a throughput capacity of 3 to 8 tons/h depending on the type of film being processed. Its large charging orifice facilitates loading even where films are large and bulky, as they tend to be at times. The machine's point blade rotor, measuring approx. 2,800 mm in length, is driven by two 132 kW electric motors. At a step less variable operating speed of around 100 r.p.m., the rotor – carrying 86 knives – draws in the film pieces particularly effectively, uniformly and with low dust release. Interchangeable screens with 50 to 100 mm hole diameters allow perfect adaptation of the shredder to each specific film charge. At the end of this pre-shredding step, shreds measuring between 50 and 100 mm are obtained.

Harald Hoffmann, Managing Director at Lindner ReSource, comments: “The system uses a belt-type power transmission. Its so-called countershaft drive carries a large safety clutch (slip clutch) which limits the maximum torque input and thus makes the shredder particularly insensitive to coarse foreign matter. With the special kind of films being processed at Soreplastic, this is particularly important since we can never rule out that, e.g., metal parts will find their way into the shredder despite all the pre-sorting.”

Vincent Sciascia adds: “The modular design allowed us to adapt, our pre-shredder perfectly to the application on hand. Its inspection and maintenance hatch can be hydraulically opened inwards, giving spacious access to the rotor area. We can thus conveniently turn or replace the knives, each of which has 4 cutting edges, or any of the eight counterknife segments. Foreign debris, too, is easily removable this way. The screen basket can likewise be opened hydraulically so that we can clean or change the screen modules quickly. All this translates into short downtimes in day-to-day operation – a key pre-requisite to cost efficiency.”

The resulting shredded film material then passes through a washing system followed by downstream wet grinding and drying. It is only after this treatment that the shred – now reduced to between 20 and 30 mm in size – are ready to enter the Erema 1716 TVEplus recycling extrusion line which, thanks to its special degassing technology, is capable of providing optimum melting, filtration and homogenization of the washed stock despite its  high initial moisture. Ultimately, the material is pelletized by an Erema HG 244 D type die-face pelletizing unit featuring a special cutting geometry and automatic air-pressurization of the pelletizing knife for maximum longevity. The overall system delivers an output capacity of approx. 1,400 kg/hr at a typical batch size of 2,500 kg.

Commissioned in November 2011, the plant has been running trouble-free and highly cost- efficient ever since.  It currently provides Soreplastic with the capacity to recycle around 20,000 tons of input material per year. Sales of the resulting high-grade PE re-pellets are assured as well, Vincent Sciascia confirms. „Our standard portfolio ranges from PE-LD through PE-LLD to customer-specific blends. This makes us the only recycler capable of offering high-quality PE-LLD from washed agricultural stretch films for film blowing applications today.“

The Lindner Group headquartered at Spittal/Austria was established in 1948 as a mechanical engineering and equipment construction company and has evolved into a competent supplier of shredding technology for industrial applications. Employing around 130 people, the Lindner Group specializes in the development, manufacture and sales of complete lines and machines for producing alternative fuels.

Its sales and customer support company Lindner reSource GmbH, based in Großbottwar/Germany, represents the Group's plastic and recycling activities. The company supplies high-powered single-shaft shredders with throughputs from 300 to 10,000 kg/h to industrial customers.

Further information:

#### Harald Hoffmann, Managing Director, LINDNER reSource GmbH

Häldenfeld 4, D-71723 Großbottwar / Germany

Phone: +49 (0) 71 48/16 05 38-0, e-mail: info@lindner-resource.com

Editorial contact and voucher copies:

Dr. Jörg Wolters, Konsens PR GmbH & Co. KG

Hans-Kudlich-Straße 25, D-64823 Groß-Umstadt / Germany

Phone: +49 (0) 60 78/93 63-0, e-mail: joerg.wolters@konsens.de

The German and English text of this press release in *doc format, as well as the

illustrations in print-quality resolution, are available for download at: 
http://www.konsens.de/lindner-resource.html

|  | A challenge to any recycler: collected post-consumer agricultural film |
| --- | --- |
|  | A Lindner reSource Power Universo 2800 pre-shredder with downstream separation of coarse impurities forms the first station in Soreplastic's film recycling line. |
|  | The Erema 1716 TVEplus recycling extrusion line in use at Soreplastic |