# Ultrasonic welding in medical technology

Rinco Ultrasonics' Electrical Motion welding machine meets the most stringent requirements for precision, traceability and cleanliness

The Electrical Motion ultrasonic welding machine's electrical drive means it is capable of meeting the high quality requirements applicable in medical technology. Photo: Rinco Ultrasonics AG

Romanshorn, Switzerland, June 2017 – The Electrical Motion ultrasonic welding machine (working frequency 20 kHz) from Rinco Ultrasonics, the Swiss ultrasonic welding specialist, meets the demanding requirements for tight tolerances, traceability and hygiene which are typical of medical technology. Its electrical drive and control by means of an ultrasonic generator with built-in industrial PC ensure particularly accurate sonotrode control, while welding force and rate are also accurately adjustable. This results in consistency and reproducibility of the welding, punching, cutting and sealing operations carried out on thermoplastic mouldings and films, nonwovens and synthetic textiles.

Thanks to its electrical drive, the Electrical Motion's welding force, rate and speed are very much more accurately controllable than on a conventional, pneumatically driven machine. Distance mode, for instance, permits positioning with an accuracy of 0.01 mm. It is also possible to set limit values on the machine which trigger an alarm or stop the machine in order to ensure reproducibility and thus quality. The defined welding parameter data records and welding results can be exported from the machine's internal storage to an external data storage medium to enable compliance with the medical technology sector's audit and documentation requirements. In addition, a non-erasable audit trail records all events, for example maintenance operations and changes to parameters, for quality improvement and traceability purposes. Different hierarchical levels of authorisation can be set, so ensuring that only authorised persons can change parameters or acknowledge events. The Electrical Motion has ISO Class 6 certification for clean room manufacture.

The machine's electrical drive also means that the sonotrode's starting position can be freely selected. As a result, unlike with a pneumatic drive, the sonotrode does not have to be returned to zero position for each welding cycle. Depending on the geometry of the object being welded, this can result in distinctly shorter cycle times. The integrated quick-change system means that tools can be swapped within a few minutes, so minimising downtime. The possibility of using existing tools on both the tried and trusted Dynamic 3000 series and the Electrical Motion is a further benefit for many users. To ensure still higher availability of what is already a highly reliable machine, the Electrical Motion can also be installed for remote access service from Rinco headquarters. When required, a service technician can be on site within 48 hours.

RINCO ULTRASONICS AG (www.rincoultrasonics.com), headquartered in Romanshorn, Switzerland, has been a specialist in the design and manufacture of ultrasonic welding machines and ultrasonic cutting equipment since it was founded in 1976. RINCO products are used for the reliable welding of plastic components and for cutting foodstuffs and synthetic textiles. With its many years of expertise in the development of innovative solutions and consulting in the field of application technology, RINCO is an acknowledged and reliable partner to many companies in the automotive industry, medical technology, textile and food processing, packaging, electrical engineering, plant and machinery construction, telecommunications and household & leisure. RINCO ULTRASONICS has been a member of the internationally active CREST GROUP since 1997 and, with its own branches and representatives in over 40 countries around the globe, offers outstanding proximity to the customer.

■■■

# Further information:
Martina Egger, Marketing & Communication
RINCO ULTRASONICS AG, Industriestraße 4, CH-8590 Romanshorn 1
Phone: +41 71 466 41 - 34, Fax: - 01, Email: m.egger@rincoultrasonics.com

Editorial contact and voucher copies: 
Dr.-Ing. Jörg Wolters, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25,  D-64823 Groß-Umstadt – www.konsens.de

Phone: +49 (0) 60 78 / 93 63 - 0,  mail@konsens.de

Dear colleagues, 
News releases from Rinco Ultrasonics, including text (German and English) and photos in print-ready resolution are available for download from: www.konsens.de/rinco.html