Extended Purell Portfolio allows tailor-made solutions for pharmacy and healthcare products

Augsburg, November 2009

Ultrapolymers (www.ultrapolymers.de) continues to extend its portfolio of LyondellBasell’s Purell PE, PP and metocene PP grades, which are tailored to pharmacy and healthcare applications. This step underlines the plastics distributor’s commitment to its role as an experienced and reliable provider of top quality raw materials which comply with the highly-demanding purity specifications of these particular industries. Continuous additions to the company’s range of products, including the recently-developed grades Purell RP374R and Purell ACP6031D, combined with direct access to its experienced consultants, provide a strong basis for OEMs and converters alike to find the most suitable material solution for their challenging applications.

- Purell RP374R is a recently-introduced, FDA-approved PP random copolymer with high transparency and a multitude of possible packaging applications in pharmacy, healthcare, laboratory, and diagnostics. Further advantages include its ease of processing as well as its high flexibility. Purell RP374R can be sterilized with ETO in an autoclave. Typical applications include empty disposable three-part-syringes.

- Purell ACP6031D is a PE-HD grade specially designed for extrusion blow-moulding and injection blow-moulding applications, where high stiffness and environmental stress resistance are crucial. Its very low level of antioxidant additives makes this new grade a first choice for direct water contact. Further applications include injection blow-moulded packaging units, e. g. for tablets.

As Rainer Konrad, product manager for Purell at Ultrapolymers confirms: “Manufacturers of pharmaceutical and healthcare packaging must be able to rely on the secure and consistent long-term delivery of raw materials as specified for a particular application, as any change in formulation would require new, time-consuming approval runs. Purell provides this security. LyondellBasell ensures the continuously high quality level of its polymers as well as a global security of supply. Beyond this, Ultrapolymers can provide additional assurance: Should an unforeseen shortage of a particular Purell grade occur, the distributor has access to its own extensive warehouse stock, enabling  its customers to continue their production.”

Purell is a trademark of LyondellBasell

Ultrapolymers Deutschland GmbH, Augsburg/Germany, supplying customers in Germany, Austria and Switzerland, is part of the pan-European plastics distributor Ultrapolymers Group NV, Lommel/Belgium. The company’s portfolio includes polyolefines from LyondellBasell, polystyrene from INEOSNOVA, polyamide from Ascend and Ravago, long fibre reinforced thermoplastics from FACT, bio-based polymers from FKuR, rotational moulding polymers from Borealis and LyondellBasell, engineering polymers from LG Chem, commodities, masterbatch and additives, the Colorflexx service package for self-colouring of ABS as well as customer specific compounds. Headquartered in Augsburg, Ultrapolymers Deutschland runs sales offices in Bielefeld, Kierspe, Nurnberg, and Stuttgart. Austrian and Swiss customers are supported from the distributor’s Augsburg office.

| Voucher copies and editorial contact: Konsens PR GmbH & Co. KG, Dr. Jörg Wolters, Hans-Kudlich-Str. 25 D-64823 Groß-Umstadt Tel.: +49 (0) 60 78/93 63-13 E-Mail: mail@konsens.de | Please find this press release as Word file for download under: http://www.konsens.de/ultrapolymers.html |
| --- | --- |

Based on a comprehensive portfolio of Purell PE, PP and metocene-PP grades from LyondellBasell the plastics distributor Ultrapolymers Deutschland offers its customers high purity packaging materials for demanding pharmaceutical and health care applications.

Photo: Ultrapolymers Deutschland